## Slide 1: Standardizing Zones Across the Storage Ecosystem
Sponsored by NVM Express™ organization, the owner of NVMe™, NVMe-oF™ and NVMe-MI™ standards

## Slide 2: Speaker
Dave Landsman
Director of Industry Standards

## Slide 3: Beyond Random IO – New Use Cases for NVMe
Over past couple years, industry debate on Open Channel vs. “Traditional” SSDs
Debate is really about the emergence of two new SSD use case categories
  Write Amp Reduction
  Focus on Capacity/Cost
  Host/SSD collaboration on GC and Wear Leveling
  IO Isolation
  Focus on Latency/QoS
  Host control over SSD physical topology
New: Zoned Namespaces
Application 1
Application 2
Application 3
ZNS SSD Controller
New: Endurance Group Mgmt
  Enable standard provisioning of topology isolation use cases
NVMe 1.4: IO Determinism
  NVM Sets & Endurance Groups
  Predictable Latency Mode
Zone 0
Zone 1
Zone 2
Zone 3
Zone n
Write pointer
Write commands
advance write pointer
Reset write pointer commands
rewind the write pointer
All Writes Sequential
LBA space divided into fixed size ranges
Application 1
Application 2
Application 3
ZNS SSD Controller
Deterministic
Non-Deterministic
Deterministic
Non-Deterministic

## Slide 4: Zoned Block Storage already in HDDs
SMR (Shingled Magnetic Recording)
  Enables areal density growth
  Causes magnetic media to act like flash
    Data must be erased to be re-written
Zoned Block access for HDDs
  Drive formatted into fixed sized regions
  Host/Device enforce sequential writes in LBA space to mitigate RMW effects of SMR
  Zoned Block interface standardized in T13/T10
    Zoned ATA Commands (ZAC): SATA
    Zoned Block Commands (ZBC): SAS
Take advantage of SMR capacity growth

## Slide 5: Why Zoned Block Storage for SSDs
TLC & QLC increases capacity but at cost of
  Less endurance
  Lower performance
  More DRAM to map higher capacity
Zoned Block access for SSDs
  SSDs are intrinsic Zoned devices due to flash characteristics
  Host/SSD cooperate (distributed FTL) using sequential access
  No complex topology provisioning; Zones are logical
  Reduces write amplification and internal data movement
Result
  Reduced wear
  Improved latency outliers and throughput
  Reduced DRAM in SSD (smaller L2P)
  Reduced drive Over Provisioning
Take advantage of TLC/QLC capacity growth
Application 1
Application 2
Application 3
Conventional SSD Controller
LBA Space
Application 1
Application 2
Application 3
ZNS SSD Controller
Zoned LBA Space
Zone

## Slide 6: Why Zoned Block Storage for SSDs?
Modified Applications
SW ecosystem optimized at multiple levels
Foundation is the Zoned Block Device
Different optimization paths
  App -> POSIX File -> Unmodified FS -> dm-zoned -> ZBD
  App -> POSIX File -> Modified FS -> ZBD
    FS knows which LBAs in which file
  Modified App -> ZBD
    No file system; app knows most about data; e.g., may use zones as containers for objects
We are adding changes for ZNS
Synergy w/ ZAC/ZBC software ecosystem
SCSI/ATA SMR HDD
Unmodified Applications
Logical Blk Device
(dm-zoned)
FS with ZBD Support
(f2fs, btrfs, xfs)
Unmodified FS (xfs)
User Space
Linux Kernel
Block Layer (ZAC/ZBC)
Block Device I/F
POSIX File I/F
Zoned Block Device I/F
RocksDB
LevelDB
CEPH
BluesStore
Level of Optimization
LBA or file based GC
Data structure driven GC
+ ZNS
+ ZNS
+ ZNS
+ ZNS
+ ZNS
+ ZNS SSD

## Slide 7: Zoned Namespaces TP
Inherits NVM Command Set
Namespace divided into fixed sized Zones
  Sequential Write Required is only zone type supported for now
Aligned to host-managed ZAC/ZBC model, with some SSD optimizations
  Zone Capacity
  Zone Append
Ongoing in the NVMeTM working group
Zone 0
Zone 1
Zone 2
Zone 3
Zone X
Write pointer
Write commands
advance write pointer
Reset write pointer commands
rewind the write pointer
LBA space divided into sequentially written ranges
Sequential Write Required

## Slide 8: Zoned Namespaces TP
ZNS model similar to ZAC/ZBC
  States: Empty, Full, Implicit Open, Explicit Open, Closed, Read Only, Offline
  State Changes: Write, Zone Management Command (Open, Close, Finish, Reset), Device Resets
Zone Size vs. Zone Capacity(NEW)
  Zone Size is fixed
  Zone Capacity is variable
Zone Capacity
Zone Capacity (E.g., 500MB)
Zone Size (e.g., 512MB)
Zone Start LBA
Zone X
Zone X - 1
Zone X + 1
ZNS State Machine

## Slide 9: Zoned Namespaces TP
ZAC/ZBC requires strict write ordering
  Limits write performance, increases host overhead
Low scalability with multiple writers to a zone
  One writer per zone -> Good performance
  Multiple writers per zone -> Lock contention
Performance improves somewhat by writing to multiple Zones
With Zone Append, we scale
  Append data to a zone with implicit write pointer
  Drive returns LBA where data was written in zone
Zone Append
1500
1300
1100
900
700
500
100
-100
300
1
2
3
4
Number of Writers
Metal (i7-6700K, 4K, QD1, RW, libaio)
1 Zone
4 Zones
Zone Append
K IOPS

## Slide 10: Zoned Namespaces TP
How does Zone Append work?
No host serialization; higher queue depth
Scalable for HDDs and SSDs
Host serializes I/O, forces low queue depth
Insignificant lock contention when using HDDs
Significant lock contention when using SSDs
4K Write0
8K Write1
16K Write2
WP
(after W0)
WP
(after W1)
WP
(after W2)
Zone
Zone Write Example
Queue Depth = 1
4K Write0
8K Write1
16K Write2
WP
(after all writes)
Zone
Zone Append Example
Queue Depth = 3

## Slide 11: Summary – Zoned Namespaces
Standardizes interface for key evolving SSD use case
  Sequential-write centric workloads
  Host/SSD cooperate on GC and WL
Enables lower cost solutions
  Reduced wear
  Reduces SSD DRAM
  Reduced overprovisioning
SW model synergy w/ SMR HDD ecosystem
Specification nearing completion in NVMeTM WG

## Slide 12
Questions?

## Slide 13: BACKUP

## Slide 14: RocksDB and Zoned Block Devices
Embeddable key-value persistent store where keys and values are arbitrary byte streams.
Optimized for fast storage, many CPU cores and low latency
Based on Log-Structured Merge (LSM) Tree data structure
The LSM structure aligns with Zones, and enables significant optimizations
Integrates with MySQL databases (MyRocks)
Patches are in progress
…
…
L0
L1
Ln
memtable
Persisted
In memory
sstable
Hot Data
A
Z
Z
A
Z
A
Z
A
A
Z
sync
compaction
compaction
Append-only
A
Z
Most Updated
Least Updated
e.g. 64MB
e.g. 128MB
e.g. 1G
e.g. 100G
Grows 10X
Cold Data
RocksDB

## Slide 15: Ceph and Zoned Block Devices
Distributed File-System providing object, block and file-level storage.
Enable Ceph to utilize Zoned Block Devices
Ceph Bluestore removes the local file system from the equation
  BlueFS backend writes data directly to the block device and can handle the sequential constraints
  RocksDB uses LSM-trees that naturally generate no/few random updates and can easily be stored on ZBDs as well
Zones or group of zones can map to natural failure domains that may be smaller than the whole device
  Mapping OSDs to such failure domains would naturally ensure that recovery from failure would involve less network utilization and fewer I/Os
Zettabyte Infrastructure
CEPH
BlueStore
data
metadata
BlueFS
RocksDB
FileStore
leveldb
data
omap
SMR HDD
ZBC/ZAC
ZNS SSD
Logical Block Device
(dm-zoned)
XFS with
ZBD support
SCSI/ATA
Legacy XFS
Linux
Kernel
Block Layer
NVMe

## Slide 16: Zoned Namespaces TP
For NVMeTM devices that implement the Zoned Command Set, there is optional support for:
  Variable Capacity
    The completion of Reset Zone command may result in a notification that zone capacity has changed
  Zone Excursions
    The device can transition a zone to Full before writes reaches the Zone Capacity. Host will receive an AEN and write failure if writing after the transition
If device implements, the host shall implement as well
  Incoherent state model if not – Software should be specifically be written to know that zone capacity can change, or writes may suddenly fail
Attributes: Zone Excursions & Variable Capacity
Zone Capacity (E.g., 500MB)
Zone Size (e.g., 512MB)
Zone Start LBA
Zone X
Zone X - 1
Zone X + 1
Zone Excursion